UNIVERSAL WALL PUTTY THICK

DESCRIPTION

Acrylic emulsion based thick surface smoothing putty used for background preparation of water based paints in exterior walls.

APPLICATION

Used for filling the pores in the mineral based surfaces in exterior sides like concrete, light concrete, aerated concrete or plaster.

FEATURES

- High adherence and breathing ability.

- Forms a very durable, smooth and non-chalking surface.

- Decrease in waste of paint.

- Not much chalking during sanding.

- Smoothing the surface with maximum 2 coats.

- Water-based, odor-free; harmless to human health and environment.

SURFACE PREPARATION

- Clean the surface of all dirt, oil, blistered paint and dust.

APPLICATION INSTRUCTIONS

- UNIVERSAL WALL PUTTY THICK must be mixed thoroughly prior to application.

- UNIVERSAL WALL PUTTY THICK must be applied with steel spud, as one or two coats depending on the surface roughness.

- 24 hours after the application of the putty, the defects on the surface and spud marks must be smoothed with sandpaper.

- The environment of application must be kept between +5 °C to +35 °C within 24 hours during and after the application.

DRYING TIME

The contact time is 4-6 hours, and through-dry time is 24 hours in environment of 23oC.

PACKING

25 kg

THEORITICAL CONSUMPTION

Depending on surface smoothness, porosity and application methods, for a single coat application:

With 1 liter of paint 2,2 – 4,5 m² area,  with 1 kg of paint 1,25 – 2,5 m2 area can be painted. Paint consumption for 1 m2 area is 230 - 460 ml and 400 - 800 gr.

STORAGE

Store in enclosed packaging for 1 year between +5oC to +35oC.

PRECAUTIONARY STATEMENTS

P 102                   Keep out of reach of children.

P 301+ P 310     IF SWALLOWED: Immediately call a POISON CENTRE or doctor/physician.

Note: For more technical information, please check the Material Safety Data Sheet (MSDS) of the product.